## Slide 1
Group K2
Ali Fuat Şahin
Can Uludoğan
Egemen İlikmen
Faysal Turkistani
Furkan Evci
Mehmet Furkan Doğan
Osman Berkin İnci
CONTROL SYSTEM DESIGN OF MICROPROCESSOR-CONTROLLED PROSTHETIC KNEE JOINT
Fall 2022-2023 ME 407 Mechanical Engineering Design

## Slide 2
Definition
Designing a control system that provides adjustable damping according to the gait cycle phases.
Motivation
Allow transfemoral amputees to experience freedom and convenience in their daily activities.
Problem Definition & Motivation

## Slide 3
Requirements & Performance Criteria
Requirements
Design the control system to work on the Ottobock C-leg Prosthetic Knee
Correctly identify gait cycle phases and adjust damping accordingly
Adjust damping to adapt to different users
Adjust damping to adapt to different walking speeds
Safety precaution mechanism for unexpected user behavior
Effective energy consumption
Performance Criteria
Rotate knee between 0 and 130 degrees
Walking speed up to 2 m/s
Provide standing, walking and running modes
Battery enough to walk 15000 steps with 1.6 m/s
Control system response delay time less than 5 ms
User interface and IoT
Control system cost less than $ 350
Control system less than 300 grams

## Slide 4
3D CAD Model ( Whole Assembly )

## Slide 5
3D CAD Model ( Valve System)

## Slide 6
Circuit Working Principle

## Slide 7
Final System Control Circuit

## Slide 9
Cause of Energy Consumption | Number of Steps | Energy Consumption
Stand-by mode | 1 | 0.05 mWh
1 Valve Motor | 1 | 0.2 mWh
2 Valve Motors | 1 | 0.4 mWh
Total | 1 | 0.65 mWh
 | 15000 | 9750 mWh
Available Energy |  | 12000 mWh
Energy Consumption

## Slide 10
Communication with User

## Slide 11
Simulink Walking Simulation

## Slide 12
Hydraulics Simulation

## Slide 15
Safety Precaution

## Slide 16
Modifications Between Mock-Up and Detailed Design

## Slide 17
Fuzzy Logic Design

## Slide 18
Membership Functions of Gait Phase

## Slide 21
Parts Bought / Manufactured

## Slide 22
Pipe

## Slide 23
Strain Gage Holder

## Slide 24
Experience Gained
Engineering analysis and simulations allowed prediction on how the design will perform under different conditions.
Identify problems early in the design process.
Testing provided view on the performance of the design in real world conditions and helped to validate and invalidate assumptions and analysis results.
Better understanding of design and limitations.
See potential areas for improvement

## Slide 25
Fuzzy logic optimization (tuning) can be done using machine learning to get more accurate and precise results.
Machine Learning Implementation
Inertial Measurement Unit (IMU)
To increase the variety of inputs that can be fed into the control system IMUs can be used.